## Slide 1: IoT for environmental monitoring
Hand’s on workshop
Innovation Engine
Notes: Pieter Bruegel the Elder-
The Harvesters, 1565

## Slide 2
  TODOs
  Adapt content to 8266
  Include wiring process for three sensors:
    Include code for 2.5 to 10 um.
    CO
  Relate to citizen science
  Include NodeRED example
  Include Python example
  Explain sensor principle

## Slide 3: Introduction
Welcome ! This workshop will introduce you to the Internet of Things and the IBM Watson Internet of Things Platform (Watson IoT).
Watson IoT is a fully managed, cloud-hosted service to manage IoT devices and makes it simple to derive value from them. An IoT device can be a sensor, an actuator, a gateway or something else.
Through this guide, you will be able to connect an IoT device to Watson IoT, so that you can send data securely to the cloud using the open, lightweight MQTT messaging protocol. From there, you will be able to setup and manage your device, and stream its data into your online Watson IoT dashboard.
This guide walks you through the steps required to connect a sensor node to the Internet.
On the right of this slide you can find the workflow to connect your first IoT device and stream its data to the Internet. There are four main steps:

## Slide 4: A. Install the required software
1. Install and launch the Arduino IDE
Arduino IDE is an interface development environment to program your IoT device. It is free and Open Source software, and it is quite popular amongst the IoT community. You need to install the Arduino for desktop to program your device later on in this workshop.
If you are a Windows 10 users, you can get Arduino from the Windows App Store.
If you have another Windows version, MacOS, or Linux, you can download the Arduino IDE installers from ibm.biz/ArduinoSoftware. Use a recent version of the IDE (1.8.5 or later).
After installation, launch the program.
2. Installing the drivers for the ESP8266 board
To install the Arduino core for the ESP32 follow the instructions using the “Installing with Boards Manager” option in the following website:
  https://github.com/esp8266/Arduino#installing-with-boards-manager
Download and install the CH340G port driver for the board from this website:
  https://wiki.wemos.cc/downloads

## Slide 5: A. Install the required software
3. Add the ArduinoJson library
  You can add libraries to the Arduino IDE from the IDE menu option Sketch -> Include Library -> Manage Libraries…
Here, search for “ArduinoJson” and install the library by Benoit Blanchon.

## Slide 6: A. Install the required software
4. Select your board
Select “WEMOS LOLIN32” Module board from Tools > Board menu.
5 . Add the MQTT PubSubClient library
The IBM Watson IoT Platform uses the MQTT protocol, a messaging protocol. To properly communicate with the devices, you need to add the MQTT PubSubClient library to the Arduino IDE.
  Download the following zip file: https://github.com/knolleary/pubsubclient/archive/v2.3.zip
  Import the zip library to the Arduino IDE from the IDE menu option Sketch -> Include Library -> Add .ZIP Library. Here, select the downloaded .zip file.

## Slide 7: A. Install the required software
6. Register to IBM Cloud
  IBM Cloud is a cloud platform as a service (PaaS) developed by IBM. The IoT device you'll be creating, has to send it's data somewhere. This is where IBM Cloud comes in.
  If you do not have a working IBM Cloud account, you can register for a free trial at:
    https://www.ibm.com/cloud/
  After logging in, you will be asked to create an organization and space.
  Create an organization at United Kingdom with one of the suggested names.
  Name your space 'yourName dev' (change to your name) and continue.

## Slide 8: A. Install the required software
Go to IBM Cloud Dashboard and press the “Catalog” button.
In the search bar, type “Internet of things” and select “Internet of things Platform starter”.
Type your desired name in the “App name” field and press “Create” button.
Go back to the IBM Cloud dashboard. On the left menu bar, choose “Internet of Things”. Select the service you have just created.

## Slide 9: A. Install the required software
Select the Internet of Things Service from the Cloud Foundry Services “YourName-iotf-service”.
Proceed by launching the platform. This might take some time. If the progress indicator keeps loading for more than 2 minutes, please refresh your web browser.

## Slide 10: A. Install the required software
Choose Devices on the left menu and click on “Device Types”. Then click on “Add Device Type”. Make sure that you first go to “Add Device Type” before the “Add Device” section.
Name the device type “ESP32”. Proceed by clicking “Next”.

## Slide 11: A. Install the required software
Click on “Done”, leaving all Device information and Metadata tabs blank.
Click on “Register Devices”.
Guide to set your own IoT Device

## Slide 12: A. Install the required software
Now you have returned to the Add device menu. Make sure the created device type is selected. At the Device ID tab enter: ”my_first_thing” and click “Next”.
Skip the Device information page by clicking ”Next”, leaving all and Metadata tabs blank.
Guide to set your own IoT Device

## Slide 13: A. Install the required software
At the security step you can leave the Authentication Token tab blank and proceed by clicking “Next”. You will get the auto-generated token at a later step (see step 6.r).
At the summary step click “Done”.
Guide to set your own IoT Device

## Slide 14: A. Install the required software
Now you have received your Device Credentials. If you have left the Authentication Token tab blank at step 15 you will also receive your auto-generated token.
IMPORTANT: Do not forget to copy the Authentication Token. Open your notepad and paste it there. There is no option to retrieve it at a later time.
After setting up your device, from the left menu go to Security > Connection Security and click on the “🖋” button.
Guide to set your own IoT Device

## Slide 15: A. Install the required software
Under Default Rule, change Security Level to “TLS Optional”. Don't forget to “Save” your changes on top of the page
Congratulations!
You have installed the required software to set-up the IoT board and connect it to the IBM Watson Internet of Things Platform.

## Slide 16: B. Set Up the Board
7. Connect your board
Okay! We have installed all requirements. Now, we will work on the board itself. There are a wide variety of IoT devices that can be connected to Watson IoT.
In this guide we use the WeMos D1mini. This board can be easily programmed using Arduino IDE. It uses the ESP8266 architecture. It has built-in USB and WiFi connectivity, making it highly suitable for prototyping.
That is why we installed the Arduino IDE and ESP8266 drivers in previous steps.
Connect your ESP8266 board to your computer using a micro-USB cable.
Check your board is visible in the USB port. To do so, in the Arduino IDE, click on Tools/Port.
After you restart, please check if your board is visible in Arduino IDE (click on Tools/Port).

## Slide 17: B. Set Up the Board
Layout of board pins
  The pins on the edges of the board are interfaces to connect electronics such as sensors and actuators to the microcontroller.

## Slide 18: B. Set Up the Board
Place the WeMos D1mini board on your breadboard. Plug in the USB cable. Connect the 5V and Ground pins to the red and blue breadboard lines, respectively.
Breadboard usage:
The red lines on the figure above show how some vertical columns and horizontal rows are internally connected.
When power is applied to the breadboard, current flows through these internal connections.

## Slide 19: Temperature and humidity sensor (DHT11): specifications

## Slide 20: B. Set Up the Board
Connecting the T° and RH sensor
  Connect the sensor power (VCC) pin to the breadboard 5V red line.
  Connect the sensor signal (data) pin to the WeMos D2 pin.
  Also, connect the sensor signal pin to the breadboard 5V red line by using a 10K Ohm resistor.
  Finally, connect the sensor ground (GND) pin to the breadboard ground line.
  The layout should look like the one in the left picture.

## Slide 21: Dust sensor (PPD42): specifications
Pin | Description
1 | Ground
2 | Signal out: 2,5 to 10,0 um
3 | VDC, power in (5V)
4 | Signal out: 1,0 to 10,0 um
5 | Input (T1)
Pin | 5 | 4 | 3 | 2 | 1

## Slide 22: Dust sensor: specifications

## Slide 23: B. Set Up the Board
Connecting the dust sensor
  Connect the WeMos D1 pin to the sensor signal pin.
  Connect the breadboard 5V line to the sensor power pin.
  Finally, connect the sensor ground pin to the breadboard ground line.
  The layout should look like the one in the left picture.

## Slide 24: Gas sensor (MQ9): specifications
Ground
Power in

## Slide 25: B. Set Up the Board
Connecting the dust sensor
  Connect the WeMos D1 pin to the sensor signal out pin.
  Connect the breadboard 5V line to the sensor power pin.
  Finally, connect the sensor ground pin to the breadboard ground line.
  The layout should look like the one in the left picture.

## Slide 26: C. Connect the Board and Sensors to Watson IoT
Loading and running the Arduino code
Now, you have to program some code to tell the device what it actually should do. Here, you will tell the device to send the moisture value to IBM Cloud. Then, you can upload the code to the device, disconnect the device from your computer and let it measure the moisture level from anywhere in the world.
Launch Arduino IDE and open a new sketch. Replace the code in the Arduino editor with a copy of the following code:
https://github.com/santjaqo/air_quality/raw/master/WatsonIoT_workshop/IoT_DHT11_PPD42_MQ9/IoT_DHT11_PPD42_MQ9.ino
At the top of the code, include your WiFi’s network name and password. You can set a WiFi hotspot in your mobile phone if required.
Edit the values for ORG, DEVICE_TYPE, DEVICE_ID and TOKEN Upload the sketch to the ESP8266 board (Sketch>Upload->Save in default folder)
Upload the code to your board
If the error message: "Failed to open COMx" occurs (where x can be any number), go to Tools>Port and select the correct COM port.

## Slide 27: C. Visualize data on Watson IoT platform (moisture)
Visualizing moisture readings in Watson IoT.
The IoT device knows what it should do now: send all the moisture data to the IBM Cloud platform. But obviously, you want to do something with the data and visualize it. In this step, you will capture all the data within IBM Cloud and display it.
First go to Boards on the menu found in the top left of the IoT Platform website.
Create a new board.
Name your board "moisture_board", click on ”Next" and then "Submit". This board groups the IoT devices that you want to monitor together.

## Slide 28: C. Visualize data on Watson IoT platform (moisture)
Click on your newly created board and add a new card.
Select "Gauge" from the list. This card will visualize our moisture readings.
Choose the IoT device to connect to this card and click “Next”.

## Slide 29: C. Visualize data on Watson IoT platform (moisture)
Connect a new data set.
And set it up according to the image below. The event name is status (case sensitive). The property name was chosen to be moisture in the code and the name has been chosen to be moisture as well, arbitrarily. Since we are measuring humidity, the “Type” is Number, specified in percentage “%” and ranging from 0 to 100. Now, click “Next ”.
You can customize your card to your liking. For example, a large gauge meter can be chosen by choosing M in the Settings section. Click “Next”.
Here you can optionally name your card and change the color. Click ”Submit”.

## Slide 30: C. Visualize data on Watson IoT platform (moisture)
Test your humidity sensor and watch the value being monitored in your card. Congratulations! You have successfully connected your IoT to IBM Cloud!